## Slide 1
*.bck
(decomposed)
*.grid
(single block, original grid,
gi,gj,gk,xn,yn,zn,xc,yc,zc)
*.grid
(single block, new grid,
gi,gj,gk,xn,yn,zn,xc,yc,zc)
changeGrid
time.txt
*.bck2
(decomposed)
main.cpp
(original grid)
main.cpp
(new grid)
Ver 2
Boil
(original grid)
Boil
(new grid)
time.txt
Manually decrease dt

## Slide 2: For bck files of CIPCSL2
Change only conc-phi*.bck to conc-phi*.bck2.
The other variables such as conc-clr*, conc-face*, conc-sig* will be generated in main.cpp, especially made for the restart after ChangeGrid.
The code on the right is a restart part of main.cpp. When you restart after ChangeGrid, set #if 1. When you restart normally, set #if 0.
if( restart ) {
uvw .load("uvw", ts);
press .load("press", ts);
tpr .load("tpr", ts);
#if 0
/* normal start */
conc .load("conc", ts);
nucl .load("nucl", ts);
wd .load("wd", ts);
#else
/* after changeGrid */
/* load conc-phi as a scalar */
c.load("conc-phi", ts);
c.exchange_all();
/* calculate conc-sigma etc. */
conc.init();
/* zsite can be changed */
real zsite=rseed*cos(conc.get_cangle()/180.0*boil::pi);
boil::oout<<"main:change_site_z= "<<zsite<<" "<<rseed<<"\n";
nucl .load("nucl", ts, &zsite);
/* distance function from wall */
wd .load("wd", ts); // load as an initial value
sdummy = 0.0; // reset source term
di.compute();
#endif
/* calculate step in case of restart */
update_step(c, step, sdummy);
}

## Slide 3: New or updated code (github)
Add Utilities/ChangeGrid
Modify domain.h, and add domain_save.cpp
main.cpp (add dom.save(g4.dom))

## Slide 4
Scalar
dom -> xn_global(I)
dom -> yn_global (J)
dom -> zn_global (K)
Vector
u: (dom -> xc_global (I-1), dom -> yn_global (J), dom -> zn_global (K))
v: (dom -> xn_global (I), dom -> yc_global (J-1), dom -> zn_global (K))
w: (dom -> xn_global (I), dom -> yn_global (J), dom -> zc_global (K-1))
Need to output
dom -> xn_global (I)
dom -> yn_global (J)
dom -> zn_global (K)
dom -> xc_global (I)
dom -> yc_global (J)
dom -> zc_global (K)
Memo

## Slide 5
i=3
i=4
i=0,1,2
inlet
outlet
i=74
ni=78
i=75
i=76,77
Memo